## Slide 1
Building an Internet Enabled Security System
By: Michael Linnen
Twitter: @mlinnen
Blog: www.protosystem.net
Part 1 - The Introduction

## Slide 2: Sponsors

## Slide 3: Disclaimer!
This is NOT a real security system!
*This is for education purposes ONLY*
Do NOT use this as your Home Security System!

## Slide 4: The Big Picture
 | Front | Side | Back | Master Bedroom | Bedroom 1 | Bedroom 2 | 1st Floor
Doors |  |  |  |  |  |  | 
Locked |  |  |  |  |  |  | 
Windows |  |  |  |  |  |  | 
Motion |  |  |  |  |  |  | 
Doorbell |  |  |  |  |  |  | 
Alarm |  |  |  |  |  |  | 
Sleep
Away
Bedroom 1
Bedroom 2
Master Bedroom
Back door
Front door
Side door
Talk to me!
Message Broker
Azure
Worker
Master Control Panel
Web
Master Control Panel Dashboard

## Slide 5
Open Platform
Open-Source .Net Micro Framework
Open-Source Hardware
Open-Source Firmware
Rich Toolset
Visual Studio IDE
Debugging on the Netduino
Unit Testing
Flexible
Arduino Shield Compatible
Netduino
Netduino Plus
Netduino Go

## Slide 6: NETDUINO PLUS
Digital i/o Features
All 20 digital and analog pins: GPIO
Digital pins 0-1: UART 1 RX, TX
Digital pins 2-3: UART 2 RX, TX
Digital pins 5-6: PWM, PWM
Digital pins 7-8: UART 2 RTS, CTS
Digital pins 9-10: PWM, PWM
Digital pins 11-13: SPI MOSI, MISO, SPCK
Analog pins 4-5: I2C SDA, SCL
Processor and Memory
Atmel 32-bit microcontroller
Speed: 48MHz, ARM7
Code Storage: 64 KB
RAM: 42 KB

## Slide 7: Windows AZURE
Unlimited resources
  Service Bus (Messaging)
  Storage
  Computation
  Identity
  Networking (VPN)
  Web sites (10 free)
  Virtual Machines (Linux or Windows)
  Mobile Services
  Media Services
  Database Services
  Reporting Services
  Cache
  CDN
  Store
Internet Of Things Enabler
  Projecting 50 billion devices in 2020

## Slide 8: DEMO

## Slide 9
Architecture

## Slide 10
Architecture

## Slide 11
NETWORK

## Slide 12: MQTT
Features
  Lightweight
  Publish/Subscribe
  Open published protocol
How long?
  Invented in 1999
  Dr Andy Standford-Clark
  Arlen Nipper
Used By
  Facebook (messenger)
  Github
  COSM (formerly Pachube)
  RabbitMQ (MQTT Adapter)
  Websphere MQ
“MQTT is a machine-to-machine (M2M)/"Internet of Things" connectivity protocol”
http://mqtt.org

## Slide 13
MQTT
Topic
  Publish/Subscribe to Topics
  Treated as a Hierarchy
  Delineated by /
  Supports wildcard subscriptions
Message
  Represents the payload
  Binary or ASCII
TOPIC | PAYLOAD
/house1/externaldoor/front/doorbell | pushed
/house1/alarmpanel/masterbedroom/window | closed
/house1/alarmpanel/masterbedroom/window | opened
/house1/externaldoor/front/lock | unlocked
/house1/externaldoor/front/lock | locked
/house1/alarmpanel/firstfloor/setalarmstate | away
/house1/alarmpanel/firstfloor/setalarmstate | sleep
/house1/alarmpanel/firstfloor/setalarmstate | off

## Slide 14
External Door
Doorbell
Broker
Hub
Browser
MQTT
SignalR
Dashboard
Master Control Panel
Messages - doorbell
Home
Azure
Remote

## Slide 15
Messages - doorbell
Doorbell
Broker
Hub
Browser
Home
MQTT
SignalR
Dashboard
Subscribe Doorbell
Subscribe Doorbell
Master Control Panel
External Door
Azure
Remote

## Slide 16
Messages - doorbell
Doorbell
Broker
Hub
Browser
Azure
Remote
MQTT
SignalR
Dashboard
Publish Doorbell pushed
Master Control Panel
External Door
Home

## Slide 17
Doorbell
Broker
Hub
Browser
Remote
MQTT
SignalR
Dashboard
Publish Doorbell pushed
Master Control Panel
Publish Doorbell pushed
Azure
Remote
External Door
Home
Messages - doorbell

## Slide 18
Doorbell
Broker
Hub
Browser
Home
Azure
Remote
MQTT
SignalR
Dashboard
Update UI
Master Control Panel
Azure
Remote
External Door
Home
Messages - doorbell

## Slide 19
Doorbell
Hub
Browser
Azure
Remote
MQTT
SignalR
Dashboard
Master Control Panel
Home
Azure
Remote
Broker
External Door
Messages – unlock door

## Slide 20
Messages – unlock door
External Door
Doorbell
Broker
Hub
Browser
Azure
Remote
MQTT
SignalR
Dashboard
Master Control Panel
Subscribe code
Subscribe setlock
Subscribe lock
Azure
Remote
Home

## Slide 21
Messages – unlock door
Doorbell
Broker
Hub
Browser
Remote
MQTT
SignalR
Dashboard
Master Control Panel
Publish code 01
Azure
Remote
External Door
Home

## Slide 22
Doorbell
Broker
Hub
Browser
Home
Azure
Remote
MQTT
SignalR
Dashboard
Master Control Panel
Publish code 01
Azure
Remote
External Door
Home
Messages – unlock door

## Slide 23
Doorbell
Broker
Hub
Browser
Home
Azure
Remote
MQTT
SignalR
Dashboard
Master Control Panel
Publish code 01
Azure
Remote
External Door
Home
Messages – unlock door

## Slide 24
Doorbell
Broker
Hub
Browser
Home
Azure
Remote
MQTT
SignalR
Dashboard
Master Control Panel
Publish setlock unlock
Azure
Remote
External Door
Home
Messages – unlock door

## Slide 25
Doorbell
Broker
Hub
Browser
Home
Azure
Remote
MQTT
SignalR
Dashboard
Master Control Panel
Publish setlock unlock
Azure
Remote
External Door
Home
Messages – unlock door

## Slide 26
Doorbell
Broker
Hub
Browser
Home
Azure
Remote
MQTT
SignalR
Dashboard
Master Control Panel
Publish lock unlocked
Azure
Remote
External Door
Home
Messages – unlock door

## Slide 27
Doorbell
Broker
Hub
Browser
Azure
Remote
MQTT
SignalR
Dashboard
Master Control Panel
Publish lock unlocked
Azure
Remote
External Door
Home
Messages – unlock door

## Slide 28
Doorbell
Broker
Hub
Browser
Azure
Remote
MQTT
SignalR
Dashboard
Master Control Panel
Update UI
Azure
Remote
External Door
Home
Messages – unlock door

## Slide 29
MQTT
Broker
Hub
Browser
SignalR
Dashboard
Master Control Panel
Home
Azure
Remote
DIRECT Broker
NON SSL
NON SSL
NON SSL
NON SSL
SSL

## Slide 30: Gateway Broker
MQTT
Broker
MQTT
Broker
Hub
Browser
SignalR
Dashboard
Master Control Panel
Home
Azure
Remote
SSL
NON SSL
NON SSL
NON SSL
NON SSL
SSL

## Slide 31: Mission Critical
MQTT
Broker
MQTT
Broker
Hub
Browser
SignalR
Dashboard
Master Control Panel
Home
Azure
Remote
SSL
NON SSL
NON SSL
NON SSL
NON SSL
NON SSL
SSL

## Slide 32: Messaging Patterns
MQTT
Broker
Message
Router
device1
device2

## Slide 33: Messaging Patterns
MQTT
Broker
Message
Router
/device2/do/1
/device1/di/1
device1
device2
Subscribe
Subscribe

## Slide 34: Messaging Patterns
MQTT
Broker
Message
Router
/device1/di/1 true
device1
device2
Publish

## Slide 35: Messaging Patterns
MQTT
Broker
Message
Router
/device1/di/1 true
device1
device2
Publish
/device1/di/1 true
Publish

## Slide 36: Messaging Patterns
MQTT
Broker
/device1/di/1 true
device1
device2
Publish
/device1/di/1 true
Publish
Message
Router

## Slide 37: Messaging Patterns
MQTT
Broker
/device1/di/1 true
device1
device2
Publish
/device1/di/1 true
Publish
Message
Router
Publish
/device2/do/1 true

## Slide 38: Messaging Patterns
MQTT
Broker
/device1/di/1 true
device1
device2
Publish
/device1/di/1 true
Publish
Message
Router
Publish
/device2/do/1 true
Publish
/device2/do/1 true